## Slide 1
Version: 2025 May
Global Sea Level Network (GLOSS)
GOOS OBSERVING NETWORK
SPECIFICATION SHEET

## Slide 2
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Table of Contents
Mission. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Brief History. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Objectives. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Design & Data. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Network Specification. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Platform Characteristics. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Data Management. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Best Practices. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Sensor Characteristics. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Links and Additional Documents. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Supporting Graphs and Images. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Glossary. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Acronyms. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
About GOOS. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
GOOS Ocean Observing Networks. . . . . . . . . . . . . . . . . . . . . . . . . . . . .
2
2
2
3
4
6
7
9
10
11
12
13
13
14
14

## Slide 3
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Mission
The Global Sea Level Observing System (GLOSS), a component of the Global Ocean Observing System (GOOS), aims at the establishment of high quality global and regional sea level networks for application to climate, oceanographic and coastal
sea level research. The programme became known as GLOSS as it provides data for deriving the 'Global Level of the Sea Surface'.
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Description. Credit:
Brief History
Objectives
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
  ...
  ...
  ...
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
  ...
  ...
  ...

## Slide 4
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Design & Data
The main component of GLOSS is the 'Global Core Network' (GCN) of 290 sea level stations around the world for long term climate change and oceanographic sea level monitoring. The present definition of the GCN (the definition is modified every few years) is called GLOSS10.
The Core Network is designed to provide an approximately evenly-distributed sampling of global coastal sea level variations. Another component is the GLOSS Long Term Trends (LTT) set of gauge sites (some, but not all, of which are in the GCN) for monitoring long term trends and accelerations in global sea level. These will be priority sites for Global Positioning System (GPS) receiver installations to monitor vertical land movements, and their data will contribute to long term climate change studies such as those of the WMO-UNEP Intergovernmental Panel on Climate Change (IPCC).
The GLOSS altimeter calibration (ALT) set consists mostly of island stations, and will provide an ongoing facility for mission intercalibrations. A GLOSS ocean circulation (OC) set, including ntercalibrations. A GLOSS ocean circulation (OC) set, including in particular gauge pairs at straits and in polar area, complements altimetric coverage of the open deep ocean within programmes such as the World Ocean Circulation Experiment (WOCE) and Climate Variability and Predictability (CLIVAR).
Description. Credit:
GLOSS can be considered a component of IOC's Global Ocean Observing System (GOOS), and particularly as a major contributor to its Climate and Coastal Modules. Information on the links between GLOSS and other IOC activities can be obtained from the IOC's web site.

## Slide 5
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Network Specification
Includes information on the observing network, the components, coordinating teams, mission, status and sustainability. Also describes the target, the phenomena and applications addressed, and the specific contribution of the network to the GOOS.
Network name | Global Sea Level Network (GLOSS)
Description1 | Network of Tide Gauges delivering to specifications (data, timeliness, accuracy) for characterising Global Sea Level Changes.
Governance body | GLOSS chair, GLOSS Technical Secreatary (IOC) and Steering Committee
Process for community evaluation | GLOSS Group of Experts/OCG/OOPC
Components/ Programmes2 | GLOSS
Mission | Observe the globally changing heat content of the upper ocean.
Status | Mature
Target(-s) | 300 tide gauges distributed globally, representative of broader ocean conditions
Phenomena addressed3 | Sea Level Heat Storage Extreme Events
Other important phenomena | Multi-decadal Ocean Change (SLR, 1.3mm/yr), Climate Variability (10ch), Storm Surge/Tsunamis
Sustainability* | N/A
1 https://gloss-sealevel.org/
2 https://gloss-sealevel.org/gloss-core-network
3 Definition and link

## Slide 6
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Unique contribution - coordination with other networks | Complementarity with Altimetry
GOOS delivery areas addressed4 | 
Applications addressed5 | Storm Surge/Tsunami warnings
4Definition (and link)
5Definition (and link?)
Operational services
Climate

## Slide 7
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Platform Characteristics
Specifies the platform characteristics, and temporal and spatial sampling, and the well resolved observation scales of the network.
Observing platorm(-s) used | Coastal Tide gauges
Components/ Programmes | GLOSS
Spatial sampling (standard) | Horizontal Approximately 300 stations globally: spacing variable. Vertical Sea surface
Temporal sampling (standard) | Less than hourly for all stations. 1 minute for Tsunami stations.
Space for footnotes - delete if none
Description. Credit:
Colombo, Rowlands & Chinn, & Poulose. (2002). Precise Satellite Navigation Combining Kinematic and Dynamic Techniques in Support of Remote Sensing From Space. AGU Spring Meeting Abstracts.

## Slide 8
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Data Management
Details on the network data management system for Real Time (RT) and Delayed Mode (DM) data delivery, including the team responsible for the oversight and coordination of the data system, the data center/repository, and products.
REAL TIME DATA
Oversight and Coordination | Fast: University of Hawaii RealTime: IOC Delayed Mode: GLOSS - GLOSS Station Handbook www.gloss-sealevel.org
Components/ Programmes | GLOSS
Readiness Data Management System6 | 
Data Centre / Repository | Fast: University of Hawaii Sea Level Center http://uhslc.soest.hawaii.edu Real Time: https://www.ioc-sealevelmonitoring.org/index.php
Data Delivery (Pathway) | Fast: Within Minutes-Several Hours Real Time: Within 1 week
Data Quality Control |  |  |  | 
Metadata Readiness Level7 |  |  |  | 
Timeliness/Latency | Fast: Within Minutes-Several Hours Real Time: Within 1 week
Products/Users8 | N/A
6Definition
7Definition
8Definition

## Slide 9
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Data Management
DELAYED MODE DATA
Oversight and Coordination | Fast: University of Hawaii RealTime: IOC Delayed Mode: GLOSS - GLOSS Station Handbook www.gloss-sealevel.org
Components/ Programmes | GLOSS
Readiness Data Management System |  |  |  | 
Data Centre / Repository | University of Hawai'i Sea Level Center - GLOSS Fast-Delivery Center British Oceanographic Data Centre Publish Data Library - GESLA British Oceanographic Data Centre - GLOSS Delayed-Mode data Data streams are currently accessible from https://gloss-sealevel.org/data but an action from the GLOSS Group of Experts 18th meeting is to create a unified front end for data delivery.
Data Delivery (Pathway) | N/A
Data Quality Control |  |  |  | 
Metadata Readiness Level |  |  |  | 
Timeliness/ Latency | N/A |  |  | 
Products/Users | Mean Sea Level Data (Permanent service for Marine Sea Level, PSMSL) www.psmsl.org/data/
Space for footnotes - delete if none

## Slide 10
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Best Practices
Title of the Best Practice | GOOS Endorsed (Yes/No) | Description | Link to the OBPS repository
 |  | UNESCO/IOC. 2002. Manual on sea-level measurement and interpretation. Volume III: Reappraisals and recommendations as of the year 2000. Intergovernmental Oceanographic Commission of UNESCO, IOC Manuals and Guides No.14, vol. III, Paris | 
 |  | UNESCO/IOC. 2006. Manual on Sea-level Measurements and Interpretation, Volume IV: An update to 2006. Intergovernmental Oceanographic Commission of UNESCO, IOC Manuals and Guides No.14, vol. IV, Paris. | 
 |  | UNESCO/IOC (2016): Manual on sea level measurements and interpretation, Vol. V: Radar gauges. IOC Manuals and Guides, 14, JCOMM technical report no. 89. | https://unesdoc.unesco.org/ark:/48223/pf0000246981
 |  | UNESCO/IOC (2020) Quality Control of in situ Sea Level Observations: A Review and Progress towards Automated Quality Control, Vol. 1. | http://dx.doi.org/10.25607/OBP-854
A best practice is a methodology that has repeatedly produced superior results relative to other methodologies with the same objective: to be fully elevated to a best practice, a promising method will have been adopted and employed by multiple organizations. Best practices are listed in the Ocean Best Practices System (OBPS) repository9.
9 https://www.oceanbestpractices.org/ocean-best-practices-systems/repository/

## Slide 11
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Sensor Characteristics
Details on the commonly used sensors, the variables measured, including GOOS Essential Ocean Variables* (EOVs) and GCOS Essential Climate Variables* (ECVs), supporting variables* and the level of sensor readiness.
Sensors/ Technique | Measured variables | Supporting variables | EOVs10 / ECVs11 (measured/ derived) | Readiness of sensor/ technique12 | Standard/ Commonly used sensor13
Tide Gauge | Sea Level (relative to land) | N/A | Sea Surface height | Mature | N/A
10 List of GOOS EOVs: https://goosocean.org/what-we-do/framework/essential-ocean-variables/
11 List of GCOS ECVs: https://gcos.wmo.int/site/global-climate-observing-system-gcos/essential-climate-variables
12 See FOO* readiness table: https://www.ioccp.org/images/D2backgroundDoc/Framework%20for%20Ocean%20Observing.pdf
13 If relevant to network/element

## Slide 12
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Links and Additional Documents
Background Information | http://www.gloss-sealevel.org/
Products & Visualizations | Links to various data types: http://www.gloss-sealevel.org/data/#.VRFlLfnF_LE
Data References | http://www.ioc-sealevelmonitoring.org/list.php http://www.ioc-sealevelmonitoring.org/gloss.php

## Slide 13
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Supporting Graphs and Images
Description. Credit:
Figure 1: Current status of the Global Sea Level Observing System network (core network). The GLOSS core network status as of December 2010 can be summarised in terms of the latest data received by the PSMSL for each station in the network. The network is divided into four 'Status Categories', category 1 being the most "operational and up-to-date". GLOSS reference sections (Operational Platforms).

## Slide 14
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet
Glossary
Essential Climate Variable (Essential Climate Variables): a physical, chemical or biological variable or a group of linked variables that critically contribute to the characterization of Earth’ s climate.
Essential Ocean Variable (Essential Ocean Variables): a measurement needed to assess ocean state and variability for important global ocean phenomena, and to provide essential data for applications that support societal benefit.
Framework for Ocean Observing (FOO) is a guide written for the ocean observing community to institute an integrated and sustained global observing system that addresses the variables to be measured, the approach to measuring them, and how their data and products will be managed and made widely available
OceanOPS provides international coordination and support to the ‘global’ observing networks through leading metadata quality control, observing system visualization and metrics, tools for network performance monitoring , and supporting opportunities for cross-network deployment of instruments.
Supporting variables: Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Sustainability: Provides strengths, weaknesses, opportunities, and threats to sustainability and define long term -30 years.
Acronyms
ALT – Altimeter calibration
CLIVAR – Climate Variability and Predictability
GCN – Global core Network
GLOSS – Global Sea Level Network
GPS – Global Positioning System
IPCC – Intergovernmental Panel on climate Change
LTT – Long Term Trends
OCG – Observations Coordination Group
OOPC – Ocean Observations Panel for Climate
PSMSL – Permanent Service for Marine Seal Level
WOCE – World Ocean Circulation Experiment

## Slide 15
About GOOS
The Global Ocean Observing System (GOOS) is the global infrastructure that brings together countries, institutions, scientists, and ocean professionals to
observe the ocean in a coordinated, sustained, and globally integrated way.
Established in 1991 and co-sponsored by UNESCO’s Intergovernmental Oceanographic Commission (IOC), the World Meteorological Organization (WMO), the United Nations Environment Programme (UNEP), and the International Science Council (ISC), GOOS is the backbone of global ocean observing.
GOOS Ocean Observing Networks
Argo
Automated Shipboard Aerological Programme (ASAP) - SOT
Global Drifter Array - DBCP
Global Sea Level Network (GLOSS)
Global Ocean Ship Based Hydrographic Investigations Program (GO-SHIP)
Global High Frequency Radar Network (HF Radar)
Moored Buoys - DBCP
OceanGliders
OceanSites
Ship of Opportunity Program (SOOP) - SOT
Tsunami Buoys - DBCP
Voluntary Observing Ship (VOS) - SOT
Emerging networks:
Fishing Vessel Ocean Observing Network (FVON) (emerging)
Surface Ocean CO2 Observing Network (SOCONET) (emerging)
SMART Cables (emerging)
Surface UNcrewed Fleet (emerging)
All GOOS Ocean Observing Network specification sheets can be accessed here:
Link to be added when all specification sheets are finalized
Global Sea Level Network (GLOSS)
GOOS Observing Network Specification Sheet

## Slide 16
Content developed by .......
The designations employed and the presentation of material throughout this publication do not imply the expression of any opinion whatsoever on the part of UNESCO concerning the legal status of any country, territory, city or area or of its authorities, or concerning the delimitation of its frontiers or boundaries. The ideas and opinions expressed in this publication are those of the authors; they are not necessarily those of UNESCO and do not commit the Organization.
Published in 2025 by the Global Ocean Observing System Programme under the Intergovernmental Oceanographic Commission of UNESCO, 7, Place de Fontenoy, 75352 Paris 07 SP, France
©UNESCO
For bibliographic purposes, this publication should be cited as follows: Observing Network Specification Sheet, Network Name (Year), Global Ocean Observing System (GOOS). GOOS Report No.XXX, v.X